## Slide 1
Tutorial : interfacing an I2C LCD Display with STM32L4
Jean-Christophe Toussaint Phelma Grenoble-INP France
STM32L4 Series
The HD44780 is a widespread common LCD controller allowing to drive various formats
of LCD displays made of 1 line with 8 characters (1X8), 2X16, 2X20, 4x20 or others.
It can be driven through a PCF8574 device which provides general-purpose remote
I/O expansion by way of the I2C interface [serial clock (SCL), serial data (SDA)].
The following equipment is used
- NUCLEO-L476RG Board or equivalent and a HD44780 LCD with a PCF8574 expander
- Eclipse with the necessary packages for Nucleo boards installed
- OpenOCD or STLink USB Driver - STM32CubeMX

## Slide 2
Generating the config. files from STM32CubeMX.
  Open STM32CubeMX and open a new project.
  Select the Nucleo-L476RG from the Boards tab
  HIS Resonator Clock with PLLCLK is selected by default

## Slide 4
  Go to Project Settings > Generate code
  Enter a project name and select SW4STM32
  Generate the code and open the project in Eclipse IDE

## Slide 5: Example of Application : code to be inserted in main.c
/* Includes ---------------------*/
#include "main.h"
#include "stm32l4xx_hal.h"
/* USER CODE BEGIN Includes */
#include <i2c_HD44780.h>
/* USER CODE END Includes */
/* Private variables ------------*/
I2C_HandleTypeDef hi2c1;
UART_HandleTypeDef huart2;
/* USER CODE BEGIN PV */
/* Private variables ------------*/
/* USER CODE END PV */
/* USER CODE BEGIN 2 */
lcd_init ();
lcd_clear_display();
lcd_home();
lcd_locate(1, 1);
lcd_print_string ("Phelma");
lcd_locate(2, 1); // 2nd row
lcd_print_string ("Engineering School");
HAL_Delay (2000); // wait for 2 sec
lcd_locate(3, 1); // 2nd row
lcd_print_string ("Grenoble");
HAL_Delay (2000); // wait for 2 sec
/* USER CODE END 2 */

## Slide 6
/* Infinite loop */
/* USER CODE BEGIN WHILE */
while (1)
{
/* USER CODE END WHILE */
/* USER CODE BEGIN 3 */
lcd_clear_display();
lcd_home();
lcd_print_string ("Physics &");
HAL_Delay (2000); // wait for 2 sec
lcd_locate(2, 1); // 2nd row
lcd_print_string ("Applied Physics &");
HAL_Delay (2000); // wait for 2 sec
lcd_locate(3, 1); // 3rd row
lcd_print_string ("Electronics &");
HAL_Delay (2000); // wait for 2 sec
lcd_locate(4, 1); // 3rd row
lcd_print_string ("Materials");
HAL_Delay (2000); // wait for 2 sec
lcd_locate(4, 1); // 4th row
lcd_printf("value %d\n", 10);
HAL_Delay (2000); // wait for 2 sec
}
/* USER CODE END 3 */

## Slide 7
#include <i2c_HD44780.h>
#include <stdarg.h>
#include <stdio.h>
extern I2C_HandleTypeDef hi2c1; // change your handler here accordingly
#define SLAVE_ADDRESS_LCD (0x3F<<1) // change this to (0x27<<1) if necessary
void lcd_send_cmd (char cmd)
{
char data_u, data_l;
uint8_t data_t[4];
data_u = (cmd&0xf0);
data_l = ((cmd<<4)&0xf0);
data_t[0] = data_u|0x0C; //en=1, rs=0
data_t[1] = data_u|0x08; //en=0, rs=0
data_t[2] = data_l|0x0C; //en=1, rs=0
data_t[3] = data_l|0x08; //en=0, rs=0
while(HAL_I2C_Master_Transmit (&hi2c1, SLAVE_ADDRESS_LCD,(uint8_t *) data_t, 4, 100)
!= HAL_OK){
/* Error_Handler() function is called when Timout error occurs */
if (HAL_I2C_GetError(&hi2c1) != HAL_I2C_ERROR_AF)
{
Error_Handler();
}
}
}
I2C LCD HD4470 library for STM32

## Slide 8
/**
* @brief send data to HD44780 LCD module via I2C
* @param data
* @param None
* @retval None
*/
void lcd_send_data (char data)
{
char data_u, data_l;
uint8_t data_t[4];
data_u = (data&0xf0);
data_l = ((data<<4)&0xf0);
data_t[0] = data_u|0x0D; //en=1, rs=0
data_t[1] = data_u|0x09; //en=0, rs=0
data_t[2] = data_l|0x0D; //en=1, rs=0
data_t[3] = data_l|0x09; //en=0, rs=0
while(HAL_I2C_Master_Transmit (&hi2c1, SLAVE_ADDRESS_LCD,(uint8_t *) data_t, 4, 100)
!= HAL_OK)
{
/* Error_Handler() function is called when Timout error occurs */
if (HAL_I2C_GetError(&hi2c1) != HAL_I2C_ERROR_AF)
{
Error_Handler();
}
}
}

## Slide 9
/**
* @brief Initializes HD44780 LCD module in 4-bit mode
* @param None
* @param None
* @retval None
*/
void lcd_init (void)
{
//Initialization of HD44780-based LCD (4-bit HW)
lcd_send_cmd (0x33);
lcd_send_cmd (0x32);
lcd_send_cmd (0x28); //Function Set 4-bit mode
lcd_send_cmd (0x0c); //Display On/Off Control
lcd_send_cmd (0x06); //Entry mode set
lcd_send_cmd (0x02); //Clear Display
//Minimum delay to wait before driving LCD module
HAL_Delay(200);
}

## Slide 10
/**
* @brief Print Character on LCD module
* @param Ascii value of character
* @param None
* @retval None
*/
void lcd_printchar(unsigned char ascode)
{
lcd_send_data(ascode);
}
/**
* @brief Display of a characters string
* @param Text to be displayed
* @param None
* @retval None
*/
void lcd_print_string (char *str)
{
while (*str) lcd_send_data (*str++);
}
/**
* @brief lcd printf function
* @param string with standard defined formats
* @param
* @retval None
*/
void lcd_printf(const char *fmt, ...)
{
uint32_t i;
uint32_t text_size, letter;
static char text_buffer[32];
va_list args;
va_start(args, fmt);
text_size = vsprintf(text_buffer, fmt, args);
// Process the string
for (i = 0; i < text_size; i++){
letter = text_buffer[i];
if (letter == 10)
break;
else{
if ((letter > 0x1F) && (letter < 0x80))
lcd_printchar(letter);
}
}
}

## Slide 11: Eclipse Configuration
Parallel building with N (=3 here) processes

## Slide 12
Add ../Drivers/I2C_LCD_HD44780_Driver
to the list of include paths
Include
Paths

## Slide 13
Compile and then
Run as a STM32 runtime

## Slide 14
In Practice

## Slide 15
1. Carmine Noveillo, “Mastering STM32”, https://leanpub.com/mastering-stm32
2. Marc Laury, “A la découverte des cartes Nucleo”, Eyrolles, EAN13 : 9782212673692
3. Reference Manual for STM32L4, DM00083560.pdf
4. https://community.st.com/docs/DOC-1949-tutorial-interfacing-an-hd44780-lcd-display-with-stm32l4
5. https://community.st.com/docs/DOC-1413-tutorial-interfacing-a-stm32l053-discovery-with-an-i2c-sensor
References